## Slide 1: 1st-Order Inelastic MASTAN Extension
Cesar Marco and David Tse
Notes: DT

## Slide 2: Matlab Coding Journey for Static Analyses
CEE 280: 3D 1st Order Elastic Analysis
Ke
3D formulation
Fixed end forces
CEE 282: 2D 2nd Order Elastic Analysis
Ke and Kg
Single-step no iterations
Natural Deformation Element Force Recovery
CEE 282: 2D 1st Order Inelastic Analysis
Ke, Kg and Kp
Return Methods
Notes: DT

## Slide 3: Return Method: Regula Falsi Algorithm
Case 1: Incremental step breaches the Yield Surface
Case 2: Incremental step breaches a maximum tolerable yield surface
Source: MGZ
Notes: DT

## Slide 4: Regula Falsi Algorithm
Set the initial upper and lower limit values for tau
While loop to reduce error:
Calculate the upper and lower bound of YS
Calculate an interpolated value for the YS and tau to return step to a specified value
Update the upper or lower limit of tau by comparing their signs with the interpolated tau
Calculate Error, iterate
Use RF algorithm for each element
 Determine tau_regula for each element 
Only use the minimum value so ONLY 1 hinge yields at a time
Notes: DT

## Slide 5: Testing Code with Fixed Base Frame
Geometry + Material
Fy = 50 ksi
W30x99
10 kip lateral load on top-left joint
1st Order Inelastic Inputs:
Solution Algorithm: Single Step
Increment Size = 0.8
Max APR = 42
40 ft
12 ft
10 kips
Notes: DT

## Slide 6: Applied Load Ratios to Hinge
Hinge # | Location | MASTAN’s APR | Our Code’s APR | Difference
 | Column support | 30.284 | 30.2831 | -0.0030%
 | Column support | 32.233 | 31.7659 | -1.4491%
 | Beam end (left) | 42.0 | 41.1569 | -2.0074%
 | Beam end (right) | 42.2 | ? | N/A
1
2
3
4
2
1
3
4

## Slide 7: Displacements
Joint | Mastan’s Results |  |  | Our Code |  |  | % Difference |  | 
 | x-disp. | y-disp. | z-rot. | x-disp. | y-disp. | z-rot. | x-disp. | y-disp. | z-rot.
Top left | 1.852 | 0.02331 | -0.01017 | 1.8873 | 0.0240 | -0.0103 | 1.9% | 3.0% | 1.3%
Top Right | 1.735 | -0.02236 | -0.009499 | 1.7717 | -0.0227 | -0.0096 | 2.1% | 1.5% | 1.1%

## Slide 8: Element Forces
Element | Mastan’s Results |  | Our Code |  | % Difference | 
 | P (k) | M (k-in) | P (k) | M (k-in) | P (k) | M (k-in)
Left column | -58.69 | 15,540 | -62 | 15,533 | 5.64% | -0.05%
Right column | 58.7 | 13,930 | 64 | 15,136 | 9.03% | 8.66%
Beam | 204.7 | -14,250 | 217 | -15,462 | 6.01% | 8.51%

## Slide 9: Discussion
Event-to-event analysis is computationally intensive by 5x
Displacement , ele. forces and hinge APR % differences are < 10% with:
  different assumptions on tolerances
  use of return method when moving along YS ← MASTAN2 doesn’t use this
Analyis Type | Tic/Toc Time (s)
2D 2nd-Order elastic analysis | 3.95
2D 1st-Order inelastic analysis | 19.27
Case 2: Moving along YS requires smaller step sizes because of tolerance limits

## Slide 10: Sources of Error
Tolerances in MASTAN
  No documentation on tolerance limits, is it 0.0001 or 0.0000001?
  E.g. Element forces at 2nd Hinge at the right column support:
P = -34.08 M = -15,580
Tolerance too low → Code thinks unloading occurs for Case 2
Tolerance too high → Code doesn’t catch yielding for Case 1
MASTAN2 assumptions
  Does not use radial return for Case 2 (inc. step breaches a max. tolerable YS)
Yield Surface = 0.9999
2
Notes: When we repeat Force Recovery using tau_min, we add incremental force to force found when entire increment was taken

## Slide 11: Next Steps
Further refine return methods to:
  improve performance
  improve accuracy based on tolerance adjustments
  solve issue causing the missing 4th hinge
Continue extension to 2nd-order inelastic analysis to include geometric NL
Notes: DT

## Slide 12
Thank you!